## Slide 1: ACI Logical, resolved concrete model
Roland Ducomble - rducombl@cisco.com
TS technical Leader – CCIE 3745
Dec 2014
V2.0
Notes: V1.0 : Last updated : 10th Dec 2014
V2.0: Last update 14th Jan 2015

## Slide 2: Agenda
  What are Logical, Resolved & Concrete Models?
  Model Conversion Workflow
    Step 1: Logical Model Configured by User
    Step 2: Logical Model converted to Resolved Model
    Step 3: Resolved Model converted to Concrete Model
  Troubleshooting logic
  Visore Screenshots
  GUI Screenshots
  Class in object tree summary
  Complete example (Moquery)
  Q&A

## Slide 3: What are Logical, Resolved & Concrete Models?
  Logical Model: Model configured by User in APIC using GUI or XML/JSON API.
  Resolved Model: Model used for passing information/configuration from APIC to switches (Leaves & Spines). This model is user visible but not configurable. Its implicitly configured by APIC.
  Concrete Model: Model on which iNXOS acts on. This model is also user visible but not configurable.

## Slide 4: Model Conversion Workflow
Logical Model
Resolved Model
Concrete Model
Hardware
2. Converted by APIC
3. Converted by APIC/PE
4. Triggers sent to NXOS for
hardware programming
1.Configured by User
  1. Logical Model: Configured by User.
  2. Logical Model is converted to Resolved Model by APIC. This resolved model is then sent to the leaves & spines.
    Resolved Model exists only for sending tenant configuration such as Epg, BD, Ctx. Other configurations like Selectors are sent as is to the fabric nodes (Represented by red line).
  3. Resolved Model is converted by Policy Element (APIC agent running on leaves/spines) to Concrete Model.
  4. Creation of Concrete Model sends notifications to the iNXOS for programming hardware.
Some models are directly converted from logical to concrete by agent running on the laves & spines.

## Slide 5: Logical – Resolved – Concrete model

## Slide 6: Logical – Resolved – Concrete model MO localisation in file structure
APIC:
/aci/..
APIC:
/mit/uni/epp
/mit/uni/ctx-..
/mit/uni/bd..
Switch:
/mit/uni/epp
/mit/uni/ctx..
/mit/uni/bd..
APIC view :
/mit/topology/pod-1/node-x/sys/...
On switch:
/mit/sys/...
Switch CLI
And vsh_lc CLI

## Slide 7: Logical Model Configured By User EPg Containment Hierarchy
fvTenant
fvAp
fvAEPg
fvAEPg
fvRsBd
fvRsBd
fvBD
fvCtx
fvRsCtx
tn-coke
ap-default
epg-App
Notes: Application profile is a logical collection of Epgs participating to a provide a service. Example: “www.coke.com” could be an application profile which is provided by three EPgs named “App”, “Web” and “DB”.
fvBD: Bridge Domain
fvCtx: Private Network aka Virtual Routing and Forwarding Instance (VRF)
fvRsBd: Represents the relation to the Bridge Domain associated with the Epg.
fvRsCtx: Represents the relation to the Private Network associated with the Bridge Domain

## Slide 8
Internal deployment profile for Epg
Deployed to node / policyelement
Logical Model Converted to Resolved Model
Endpoint Profile (EpP)
fvEpPCont
fvEpP
fvLocale
fvEpP
fvLocale
fvStPathAtt
fvDyPathAtt
fvIfConn
fvIfConn
epp
fv-[uni/tn-coke/ap-default/epg-App]
fv-[uni/tn-coke/ap-default/epg-App]/node-102
fv-[uni/tn-coke/ap-default/epg-App]/node-102/stpathatt-[eth1/10]
Or
fv-[uni/tn-coke/ap-default/epg-App]/node-102/dyatt-[topology/pod-1/paths-102/pathep-[eth1/47]]
fv-[uni/tn-coke/ap-default/epg-App]/node-102/stpathatt-[eth1/10]/conndef/conn-[vlan-19]-[0.0.0.0]
or
fv-[uni/tn-coke/ap-default/epg-App]/node-102/dyatt-[topology/pod-1/paths-102/pathep-[eth1/47]]/conndef/conn-[vxlan-8912897]-[0.0.0.0]
Every Epg has an fvEpP class
There is an fvLocale for each leaf that needs the Epg
One fvStpathAtt for each Static path
One fvDyPathAtt for each host of the DVS(AVS) attached to the node in that Locale
fvIfConn represents access encaps (vlan or vxlan)
Notes: Every EPg has a corresponding EpP
EpP: An EpP is a container of summarized configuration of an EPg to be deployed on nodes.
Locale: EpP contains fvLocale which represents a node i.e. leaf or spine. fvLocale is a container of summarized configuration to be deployed on a node. – here two fvLocale will be created (one per node).
fvStPathAtt: Static Path Attachment on which the EpP has to be deployed. It could be a port/port-channel or vpc.
fvDyPathAtt: Dynamic Path Attachment on which EpP has to be deployed. It could be a port/port-channel or vpc. Its called Dynamic because its created based on the triggers coming dynamically from VM controller.
fvIfConn: Interface connectivity parameters. It represents the emcap, ip, mtu etc. information to be deployed on the path.

## Slide 9
Logical Model Converted to Resolved Model
BD and Context (fvBDDef & fvCtxDef)
  BDDef: Summarized internal representation of fvBD. Its naming property is the DN of the corresponding fvBD. It has BD identifiers like Segment ID, PcTag (policy control tag used for Contracts) etc. It also contains summarized internal representations of other BD policies like IGMP, DHCP, End Point Retention Policy etc.
  CtxDef: Summarized internal representation of fvCtx. Its naming property is the DN of the corresponding fvCtx. Like BDDef it has Ctx identifiers like Segment ID and PcTag. It also contains summarized internal representations of other Ctx policies like End Point Retention Policy etc.
uni
fvBDDef
fvCtxDef
uni/bd-[uni/tn-mgmt/BD-inb]
uni/ctx-[uni/tn-mgmt/ctx-inb]

## Slide 10
Resolved Model Converted to Concrete Model
sys
l3Ctx
vlanCktEp
l3Ctx
l2BD
l2BD
l2BD
vxlanCktEp
l2RsPathDomAtt
top::System, it’s the root of concrete model
Private network (aka VRF).
sys/ctx-[vxlan-2555904]
Bridge Domain
sys/ctx-[vxlan-2555904]/bd-[vxlan-15826914]
Encap i.e. VLAN OR VXLAN
sys/ctx-[vxlan-2555904]/bd-[vxlan-15826914]/vlan-[vlan-17]
Association from Encap to Port/Port-Channel
sys/ctx-[vxlan-2555904]/bd-[vxlan-15826914]/vlan-[vlan-17]/rspathDomAtt-[sys/conng/path-[eth1/16]]
Notes: l3Ctx (a.k.a VRF )is the concrete representation of fvCtx. Segment Id of an l3Ctx is taken from fvCtxDef.
l2BD is the concrete representation of l2BD. Segment Id of an l2BD is taken from fvBDDef.
vlanCktEp/vxlanCktEp are the encapsulations on wire. Instantiation of this object creates a VLAN on switch . For instance, these encaps are taken from fvIfConn.
l2RsPathDomAtt:
  Ports/PortChannels are considered as paths in APIC.
  VLAN/VXLAN/BD are considered as Domains.
  l2RsPathDomAtt is used for enabling a domain on a path. For instance, enabling vlan-17 on port 1/17.

## Slide 11: Troubleshooting Logic
First Step -
  Golden Rule: Always check for faults in the system. If anything fails deployment then faults are raised. For instance, if EPg deployment fails for any reason then faults will be raised on the EPg.
  Second Step
  Follow Logic : Logical Model  Resolved Model  Concrete objects
  If some links or MO are missing, get relevant dme logs (see later slide)
  Save a show tech of the 3 apics and impacted leaves
  Third Step
  Verify iNXOS using the iNXOS shell commands. (covered other sessions)

## Slide 12: Step 1 - Fault Example
  Example: User configured epg-DB on a non-existing path eth1/100. APIC validated the config and raised an “invalid-path” fault. The fault also shows the affected object.

## Slide 13: Step 2- MO tree query options
Visore – easier to browse relation – harder for tac for offline analysis
moquery – harder to browse – easiest for TAC to get part of the MIT for offline analysis
Browse to directory and get cat summary
API :
  Postman or curl to send REST GET
  Cobra SDK
  Relying on customer infra/tool unless we have VPN
GUI – a bit painful for browsing concrete model (mostly in Fabric Inventory Tab)

## Slide 14: Which Logs ?
On each APIC
(at least shard master):
/var/log/dme/log/svc_ifc_policymgr.bin.log
On APIC on which config was pushed :
/var/log/dme/log/nginx.bin.log
On leaf:
/var/log/dme/log/svc_ifc_policyelem.bin.log
And svc_ifc_eventmgr.log
Log: Watch out some logs wraps quickly check oldlog as well and creation time
to get the right one

## Slide 15: Grepping log
On APIC example looking for BD name bootcamp in tn-RD:
admin@bdsol-aci2-apic1:log> pwd
/var/log/dme/log
admin@bdsol-aci2-apic1:log> zgrep uni/tn-RD/BD-BD_bootcamp svc_ifc_policymgr.bin.*
svc_ifc_policymgr.bin.log.152.gz:<configConfMo dn="uni/tn-RD/BD-BD_bootcamp">
svc_ifc_policymgr.bin.log.152.gz:<fvBD arpFlood="no" bcastP="0.0.0.0" childAction="" descr="" dn="uni/tn-RD/BD-BD_bootcamp" lcOwn="local" mac="00:22:BD:F8:19:FF" modTs="never" monPolDn="" mtu="inherit" name="BD_bootcamp" ownerKey="" ownerTag="" pcTag="any" rn="" scope="0" seg="0" status="created" uid="0" unicastRoute="yes" unkMacUcastAct="proxy" unkMcastAct="flood">
svc_ifc_policymgr.bin.log.152.gz:<relnRelnResolveRespArgs childAction="" dn="" found="no" lcOwn="local" modTs="never" resolverDn="uni/tn-RD/BD-BD_bootcamp/rsbdToEpRet" rn="" status=""/>
svc_ifc_policymgr.bin.log.152.gz:<relnRelnResolveRespArgs childAction="" dn="" found="no" lcOwn="local" modTs="never" resolverDn="uni/tn-RD/BD-BD_bootcamp/rsigmpsn" rn="" status=""/>
svc_ifc_policymgr.bin.log.152.gz:<frmwrkReliableDeliveryResp childAction="" deliveryDn="uni/tn-RD/BD-BD_bootcamp/rsigmpsn" dn="" lcOwn="local" modTs="never" name="" rn="" status="" timestamp="1419861612726" type="rel-log" uid="0"/>
svc_ifc_policymgr.bin.log.152.gz:<frmwrkReliableDeliveryResp childAction="" deliveryDn="uni/tn-RD/BD-BD_bootcamp" dn="" lcOwn="local" modTs="never" name="" rn="" status="" timestamp="1419861612726" type="rel-log" uid="0"/>
svc_ifc_policymgr.bin.log.152.gz:<frmwrkReliableDeliveryResp childAction="" deliveryDn="uni/tn-RD/BD-BD_bootcamp/rsctx" dn="" lcOwn="local" modTs="never" name="" rn="" status="" timestamp="1419861612726" type="rel-log" uid="0"/>
svc_ifc_policymgr.bin.log.152.gz:<frmwrkReliableDeliveryResp childAction="" deliveryDn="uni/tn-RD/BD-BD_bootcamp/rsbdToEpRet" dn="" lcOwn="local" modTs="never" name="" rn="" status="" timestamp="1419861612726" type="rel-log" uid="0"/>
svc_ifc_policymgr.bin.log.152.gz:<actionUpdate dn="idm/runi-class-2818051/ctx-[res/subj-[uni/tn-RD/BD-BD_bootcamp]/reqctx-pcTag-2818051/idcon-class-2818051]" action="107" run="28" stage="52" timestamp="1419861612924">

## Slide 16: Visore ScreenShots

## Slide 17
DN of the BDDef used by this EpP
DN of the CtxDef used by this EpP
DN of the Epg corresponding to this EpP
Other EPg parameters
Here Resolved model object
For an Epg (fvEpP)
Use arrow to browse the parent/child hierarchy
Click on link to jump to different
Part of the MIT:
To the Resolved BD
To the Logical Epg

## Slide 18
fv::BDDef: Resolved object representing fv::BD
DN of the fv::BD
DN of the fv::CtxDef used by this BD
Other BD parameters

## Slide 19
fv::CtxDef: Resolved object representing fv::Ctx
DN of the fv::Ctx
Other Ctx parameters

## Slide 20
fv::IfConn: Resolved object representing interface connectivity properties.
To be applied on eth1/41 on node 101
encap

## Slide 21: Debug API
  This slide lists down the example apis which can be used to query resolved, concrete models. In general API topic will be covered as part of another session.
  Query all EpPs: http://<apic ip or leaf ip>/api/node/class/fvEpP.xml
  fvEpP is the class name of an End Point Profile. For querying other classes you can simply change the class name. For example, use fvLocale for querying all locales.
  2. Query all EpPs with their direct children:
  http://<apic ip or leaf ip>/api/node/class/fvEpP.xml?query-target=children
  3. Query all EpPs with their subtrees (subtree includes grand children and so on …):
  http://<apic ip or leaf ip>/api/node/class/fvEpP.xml?query-target=subtree

## Slide 22: Debug API (contd)
  4. Query all Path attachments under a known EpP:
  http://<apic ip or leaf ip>/api/node/mo/uni/epp/fv-[uni/tn-Coke/ap-InsiemePortal/epg-DB]/node-101.xml?query-target=children
  It looks for all path attachments under the given EpP and to be deployed on node 101.
  5. Query whole subtree under a known EpP:
  http://<apic ip or leaf ip>/api/node/mo/uni/epp/fv-[uni/tn-Coke/ap-InsiemePortal/epg-DB]/node-101.xml?query-target=subtree
  It looks for all the Mos including the subtree under the given EpP and to be deployed on node 101.

## Slide 23: GUI ScreenShots

## Slide 24: EPg Configuration: Logical Model

## Slide 25: EPg/Bridge Domain Configuration: Logical Model

## Slide 26: Bridge Domain/Private Network Configuration: Logical Model

## Slide 27: Display of Concrete Model

## Slide 28: Summary of Important Classes

## Slide 29: Logical model class
fvTenant
fvAp
fvAEPg
fvRsBd
fvBd
fvRsCtx
fvCtx
fvSubnet
…

## Slide 30: Resolved model classes
fvTenant
fvAp
fvAEPg
fvRsBd
fvBd
fvRsCtx
fvCtx
fvSubnet
…
fvCtxDef
fvBDDeg
fvEpP
fvlocale
fvStPathAtt
fvDyPathAtt
fvIfconn

## Slide 31: Resolved model classes
fvTenant
fvAp
fvAEPg
fvRsBd
fvBd
fvRsCtx
fvCtx
fvSubnet
…
On switch :
fvCtxDef
fvBDDeg
fvEpP
fvlocale
fvStPathAtt
fvDyPathAtt
fvIfconn
fvCtxDef
fvBDDeg
fvEpP
fvlocale
fvStPathAtt
fvDyPathAtt
fvIfconn

## Slide 32: Concrete model class
fvTenant
fvAp
fvAEPg
fvRsBd
fvBd
fvRsCtx
fvCtx
fvSubnet
…
On switch :
fvCtxDef
fvBDDeg
fvEpP
fvlocale
fvStPathAtt
fvDyPathAtt
fvIfconn
fvCtxDef
fvBDDeg
fvEpP
fvlocale
fvStPathAtt
fvDyPathAtt
fvIfconn
On switch(or APIC)
l3Ctx
l2BD
vlanCktEp
vxlanCktEp
l2RtDomIfConn
vlanRsPathDomAtt
vlanRsVlanEppAtt
vxlanRsVxlanEppAtt

## Slide 33: Switch CLI
fvTenant
fvAp
fvAEPg
fvRsBd
fvBd
fvRsCtx
fvCtx
fvSubnet
…
On switch :
fvCtxDef
fvBDDeg
fvEpP
fvlocale
fvStPathAtt
fvDyPathAtt
fvIfconn
fvCtxDef
fvBDDeg
fvEpP
fvlocale
fvStPathAtt
fvDyPathAtt
fvIfconn
On switch(or APIC)
l3Ctx
l2BD
vlanCktEp
vxlanCktEp
l2RtDomIfConn
vlanRsPathDomAtt
vlanRsVlanEppAtt
vxlanRsVxlanEppAtt
On switch :
Show vlans
Show system internal epm …
Vsh_lc:
Show system internal eltmc info…
Show system internal epmc info

## Slide 34: Mo logical and resolved mode relations
Tenant
fvTenant
Uni/tn-XX
BD
fvBD
Context (VRF)
fvCtx
App Profile
fvAp
Uni/tn-XX/ap-NAME
EPG
fvAEPg
uni/tn-xx/ap-XX/epg-NAME
tdn to BD
Rel to BD
fvRsBd
Rel to Ctx
fvRsCtx
tdn to Ctx
Resolved EPG
fvEpP
uni/epp/fv-[uni/tn-XX/ap-XX/epg-XX]
Resolved BD
fvBDDef
uni/ctx-[uni/tn-XX/BD-YY]
Resolved Ctx
fvCtxDef
uni/ctx-[uni/tn-XXX/ctx-CCC]
bdDn
ctxDefDn
ctxDn
bdDefDn
epgPKey
Specific Node instance
fvlocale
uni/epp/fv-[uni/tn-XX/ap-XX/epg-XX]/node-xxx
Dyn Path
fvDyPathAtt
uni/epp/fv-[uni/tn-XX/ap-XX/epg-XX]/node-xxx/dyatt-[topology/pod-1/paths-nodeid/pathep-[ethx/x]]
Static \ Path
fvStPathAtt
uni/epp/fv-[uni/tn-XX/ap-XX/epg-XX]/node-xxx/stpathatt-[ethx/x]
tdn to physical port
x/x on nodeid
Encaps -fvIfConn
uni/epp/fv-[uni/tn-XX/ap-XX/epg-XX]/node-xxx/stpathatt-[ethx/x]/conndef/conn-[vlan-xxx]..
Encaps - fvIfConn
uni/epp/fv-[uni/tn-XX/ap-XX/epg-XX]/node-xxx/dyatt-[topology/pod-1/paths-nodeid/pathep-[ethx/x]]/conndef/conn-[vxlan….]]
Notes: MO creation needs as argument:
Parent object and name for the newly created MO
Dashed relationship (function starting by Rs) takes the child
MO has argument and needs a property with the name of the
Parent dashed relation.
We can found the property value in the managed obj doc for
The child object (eg tnFvBDName is found in doc for AEPg: http://mishield-bld.insieme.local/documentation/html/MO-fvAEPg.html#diagram

## Slide 35: Mo Resolved to concrete (vlan Case here)
Resolved EPG
fvEpP
Resolved BD
fvBDDef
bd_Seg_id
Resolved Ctx
fvCtxDef
Scope_id
ctxDefDn
bdDefDn
Specific Node instance
fvlocale
Dyn Path
fvDyPathAtt
Static \ Path
fvStPathAtt
Encaps -fvIfConn
Encaps - fvIfConn
Concrete Ctx
l3Ctx
Dn – topology/pod-1/node-x/sys/ctx-[vxlan-Ctx_scope]
Concrete BD
l2BD
Dn – topology/pod-1/node-x/sys/ctx-[vxlan-Ctx_scope]/bd-[vxlan-bd_Seg_id]
bdDefDn
Vlan Encaps
vlanCktEp
Dn – topology/pod-1/node-x/sys/ctx-[vxlan-Ctx_scope]/bd-[vxlan-bd_Seg_id]/vlan-[vlan-encap]
epgDn
To logical EPG
Vlan att to EPG
vlanRsVlanEppAtt
tdn to EpP
(res EPG)
Vlan att to EPG
vlanRsPathDomAtt
tdn to Phys Port
Vlan att to EPG
l2RtDomIfConn
tdn to res Path
Physical port
nwPathEp

## Slide 36: Mo Resolved to concrete (vxlan Case here)
Resolved EPG
fvEpP
Resolved BD
fvBDDef
bd_Seg_id
Resolved Ctx
fvCtxDef
Scope_id
ctxDefDn
bdDefDn
Specific Node instance
fvLocale
Dyn Path
fvDyPathAtt
Static \ Path
fvStPathAtt
Encaps -fvIfConn
Encaps - fvIfConn
Concrete Ctx
l3Ctx
Dn – topology/pod-1/node-x/sys/ctx-[vxlan-Ctx_scope]
Concrete BD
l2BD
Dn – topology/pod-1/node-x/sys/ctx-[vxlan-Ctx_scope]/bd-[vxlan-bd_Seg_id]
bdDefDn
Vxlan Encaps
vxlanCktEp
Dn – topology/pod-1/node-x/sys/ctx-[vxlan-Ctx_scope]/bd-[vxlan-bd_Seg_id]/vxlan-[vxlan-encap]
epgDn
To logical EPG
Vlan att to EPG
vxlanRsVxlanEppAtt
tdn to EpP
(res EPG)
Vxlan att to EPG
vlanRsPathDomAtt
tdn to Phys Port
Vxlan att to EPG
l2RtDomIfConn
tdn to dyn Path
Encaps
Physical port
nwPathEp

## Slide 37: All classes together
fvTenant
fvBD
fvCtx
fvAp
fvAEPg
fvRsBd
fvRsCtx
fvEpP
fvBDDef
fvCtxDef
bdDn
ctxDefDn
ctxDn
bdDefDn
epgPKey
fvlocale
fvDyPathAtt
fvStPathAtt
fvIfConn
fvIfConn
fabricPathEp
l3Ctx
l2BD
vlanCktEp
vlanRsVlanEppAtt
vlanRsPathDomAtt
l2RtDomIfConn
nwPathEp
bdDefDn
epgDn
vxlanCktEp
vxlanRsVxlanEppAtt
vxlanRsPathDomAtt
l2RtDomIfConn
nwPathEp
epgDn
Logical
Resolved
Concrete
tdn to EpP
(res EPG)
fabricLooseNode
Notes: MO creation needs as argument:
Parent object and name for the newly created MO
Dashed relationship (function starting by Rs) takes the child
MO has argument and needs a property with the name of the
Parent dashed relation.
We can found the property value in the managed obj doc for
The child object (eg tnFvBDName is found in doc for AEPg: http://mishield-bld.insieme.local/documentation/html/MO-fvAEPg.html#diagram

## Slide 38: Complete Example – Moquery output

## Slide 39: Context
fvTenant
fvBD
fvCtx
fvAp
fvAEPg
fvRsBd
fvRsCtx
fvEpP
fvBDDef
fvCtxDef
bdDn
ctxDefDn
ctxDn
bdDefDn
epgPKey
fvLocale
fvDyPathAtt
fvStPathAtt
fvIfConn
fvIfConn
fabricPathEp
l3Ctx
l2BD
vlanCktEp
vlanRsVlanEppAtt
vlanRsPathDomAtt
l2RtDomIfConn
nwPathEp
bdDefDn
epgDn
vxlanCktEp
vxlanRsVxlanEppAtt
vxlanRsPathDomAtt
l2RtDomIfConn
nwPathEp
epgDn
tdn to EpP
(res EPG)
fabricLooseNode
Notes: MO creation needs as argument:
Parent object and name for the newly created MO
Dashed relationship (function starting by Rs) takes the child
MO has argument and needs a property with the name of the
Parent dashed relation.
We can found the property value in the managed obj doc for
The child object (eg tnFvBDName is found in doc for AEPg: http://mishield-bld.insieme.local/documentation/html/MO-fvAEPg.html#diagram

## Slide 40: Context logical (fvCtx) to Resolved Model MO (fvCtxDef)
admin@bdsol-aci2-apic1:~> moquery -d uni/tn-RD/ctx-RD
Total Objects shown: 1
# fv.Ctx
name : RD
childAction :
descr :
dn : uni/tn-RD/ctx-RD
knwMcastAct : permit
lcOwn : local
modTs : 2014-11-13T16:44:50.338+02:00
monPolDn : uni/tn-RD/monepg-RD_Monitoring
ownerKey :
ownerTag :
pcEnfPref : enforced
pcTag : 32770
rn : ctx-RD
scope : 2818051
seg : 2818051
status :
uid : 15374
admin@bdsol-aci2-apic1:~> moquery -d uni/ctx-[uni/tn-RD/ctx-RD]
Total Objects shown: 1
# fv.CtxDef
ctxDn : uni/tn-RD/ctx-RD
childAction :
descr :
dn : uni/ctx-[uni/tn-RD/ctx-RD]
knwMcastAct : permit
lcOwn : local
modTs : 2014-11-13T16:44:50.338+02:00
monPolDn : uni/tn-RD/monepg-RD_Monitoring
name : RD
ownerKey :
ownerTag :
pcEnfPref : enforced
pcTag : 32770
rn : ctx-[uni/tn-RD/ctx-RD]
scope : 2818051
seg : 2818051
status :

## Slide 41: Context Concrete MO – l3Ctx
admin@bdsol-aci2-apic1:~> moquery -c l3Ctx | grep dn | grep 2818051
dn : topology/pod-1/node-102/sys/ctx-[vxlan-2818051]
dn : topology/pod-1/node-101/sys/ctx-[vxlan-2818051]
dn : topology/pod-1/node-103/sys/ctx-[vxlan-2818051]
dn : topology/pod-1/node-104/sys/ctx-[vxlan-2818051]
admin@bdsol-aci2-apic1:~> moquery -d topology/pod-1/node-101/sys/ctx-[vxlan-2818051]
Total Objects shown: 1
# l3.Ctx
encap : vxlan-2818051
adminState : admin-up
bgpRd : 0,1,10,0,40,66,0,3
bgpRdDisp : 10.0.40.66:3
childAction :
createTs : 2014-11-12T18:35:52.449+02:00
dn : topology/pod-1/node-101/sys/ctx-[vxlan-2818051]
gsdbCtx : 0
id : 7
l3vmCfgFailedBmp :
l3vmCfgFailedTs : 00:00:00:00.000
l3vmCfgState : 0
lastChgdTs : 2014-11-12T18:35:52.449+02:00
lcOwn : local
mgmtPcTag : any
modTs : 2014-11-13T16:44:50.515+02:00
monPolDn : uni/tn-RD/monepg-RD_Monitoring
name : RD:RD
oldOperStQual : create-pending
operStQual : invalid
operState : up
oui : 0
pcEnfPref : enforced
pcTag : 32770
pending : no
prtclBmp : 96
resourceId : 5
rn : ctx-[vxlan-2818051]
scope : 2818051
secLbl : 5
status :
type : tenant
v4TibId : 5
v4TibName : base
v4TibOldOperStQual : create-pending
v4TibOperStQual : invalid
v4TibOperState : up
v4TibPending : no
v4TibValid : yes
v6TibId : 2147483653
v6TibName : base
v6TibOldOperStQual : create-pending
v6TibOperStQual : invalid
v6TibOperState : up
v6TibPending : no
v6TibValid : yes
vpnId : 0
admin@bdsol-aci2-apic1:~>
Vrf name to use in the cli RD:RD

## Slide 42: Bridge Domain
fvTenant
fvBD
fvCtx
fvAp
fvAEPg
fvRsBd
fvRsCtx
fvEpP
fvBDDef
fvCtxDef
bdDn
ctxDefDn
ctxDn
bdDefDn
epgPKey
fvLocale
fvDyPathAtt
fvStPathAtt
fvIfConn
fvIfConn
fabricPathEp
l3Ctx
l2BD
vlanCktEp
vlanRsVlanEppAtt
vlanRsPathDomAtt
l2RtDomIfConn
nwPathEp
bdDefDn
epgDn
vxlanCktEp
vxlanRsVxlanEppAtt
vxlanRsPathDomAtt
l2RtDomIfConn
nwPathEp
epgDn
tdn to EpP
(res EPG)
fabricLooseNode
Notes: MO creation needs as argument:
Parent object and name for the newly created MO
Dashed relationship (function starting by Rs) takes the child
MO has argument and needs a property with the name of the
Parent dashed relation.
We can found the property value in the managed obj doc for
The child object (eg tnFvBDName is found in doc for AEPg: http://mishield-bld.insieme.local/documentation/html/MO-fvAEPg.html#diagram

## Slide 43: BD logical (fvBD) to Resolved MO (fvBDDef)
admin@bdsol-aci2-apic1:~> moquery -d uni/tn-RD/BD-RD_BD1
Total Objects shown: 1
# fv.BD
name : RD_BD1
arpFlood : yes
bcastP : 225.1.80.16
childAction :
descr :
dn : uni/tn-RD/BD-RD_BD1
lcOwn : local
mac : 00:22:BD:F8:19:FF
modTs : 2014-11-17T17:44:51.316+02:00
monPolDn : uni/tn-RD/monepg-RD_Monitoring
mtu : inherit
ownerKey :
ownerTag :
pcTag : 16387
rn : BD-RD_BD1
scope : 2818051
seg : 16514958
status :
uid : 15374
unicastRoute : yes
unkMacUcastAct : proxy
unkMcastAct : flood
admin@bdsol-aci2-apic1:~> moquery -d uni/bd-[uni/tn-RD/BD-RD_BD1]-isSvc-no
Total Objects shown: 1
# fv.BDDef
bdDn : uni/tn-RD/BD-RD_BD1
isSvc : no
accEncap : unknown
arpFlood : yes
bcastP : 225.1.80.16
childAction :
ctxDefDn : uni/ctx-[uni/tn-RD/ctx-RD]
ctxDefStQual : none
descr :
dn : uni/bd-[uni/tn-RD/BD-RD_BD1]-isSvc-no
isPolicyEnforced : yes
lcOwn : local
mac : 00:22:BD:F8:19:FF
modTs : 2014-11-17T17:44:51.316+02:00
monPolDn : uni/tn-RD/monepg-RD_Monitoring
mtu : inherit
name : RD_BD1
ownerKey :
ownerTag :
pcTag : 16387
rn : bd-[uni/tn-RD/BD-RD_BD1]-isSvc-no
scope : 2818051
seg : 16514958
status :
type : bd-regular
unicastRoute : yes
unkMacUcastAct : proxy
unkMcastAct : flood
Binding between resolved
BD to logical BD with the bdDn
The seg id is the fabric encaps
(vxlan in fabric)
To the Resolved Ctx

## Slide 44: BD in the concrete model – l2BD
admin@bdsol-aci2-apic1:~> moquery -c l2BD | grep dn | grep 16514958
dn : topology/pod-1/node-102/sys/ctx-[vxlan-2818051]/bd-[vxlan-16514958]
dn : topology/pod-1/node-104/sys/ctx-[vxlan-2818051]/bd-[vxlan-16514958]
dn : topology/pod-1/node-101/sys/ctx-[vxlan-2818051]/bd-[vxlan-16514958]
dn : topology/pod-1/node-103/sys/ctx-[vxlan-2818051]/bd-[vxlan-16514958]
admin@bdsol-aci2-apic1:~>
admin@bdsol-aci2-apic1:~> moquery -d topology/pod-1/node-103/sys/ctx-[vxlan-2818051]/bd-[vxlan-16514958]
Total Objects shown: 1
# l2.BD
fabEncap : vxlan-16514958
accEncap : unknown
adminSt : active
bdDefDn : uni/bd-[uni/tn-RD/BD-RD_BD1]-isSvc-no
bridgeMode : mac
childAction :
createTs : 2014-11-12T17:42:13.000+02:00
ctrl :
dn : topology/pod-1/node-103/sys/ctx-[vxlan-2818051]/bd-[vxlan-16514958]
epOperSt :
fwdCtrl : arp-flood,mdst-flood
fwdMode : bridge,route
hwId : 13
id : 11
lcOwn : local
modTs : 2014-11-17T17:43:42.598+02:00
mode : CE
monPolDn : uni/tn-RD/monepg-RD_Monitoring
name : RD:RD_BD1
operSt : up
pcTag : 16387
rn : bd-[vxlan-16514958]
status :
type : bd-regular
unkMacUcastAct : proxy
unkMcastAct : flood
vlanmgrCfgFailedBmp :
vlanmgrCfgFailedTs : 00:00:00:00.000
vlanmgrCfgState : 0
Relation to the resolved BD
Using the seg id from resolved BD

## Slide 45: Epg
fvTenant
fvBD
fvCtx
fvAp
fvAEPg
fvRsBd
fvRsCtx
fvEpP
fvBDDef
fvCtxDef
bdDn
ctxDefDn
ctxDn
bdDefDn
epgPKey
fvLocale
fvDyPathAtt
fvStPathAtt
fvIfConn
fvIfConn
fabricPathEp
l3Ctx
l2BD
vlanCktEp
vlanRsVlanEppAtt
vlanRsPathDomAtt
l2RtDomIfConn
nwPathEp
bdDefDn
epgDn
vxlanCktEp
vxlanRsVxlanEppAtt
vxlanRsPathDomAtt
l2RtDomIfConn
nwPathEp
epgDn
tdn to EpP
(res EPG)
fabricLooseNode

## Slide 46: EPG logical (fvAEPg) to Resolved MO (fvEpP)
admin@bdsol-aci2-apic1:~> moquery -d uni/tn-RD/ap-App_RD1/epg-EPG_RD11
Total Objects shown: 1
# fv.AEPg
name : EPG_RD11
childAction :
configIssues :
configSt : applied
descr :
dn : uni/tn-RD/ap-App_RD1/epg-EPG_RD11
lcOwn : local
matchT : AtleastOne
modTs : 2014-11-13T16:44:50.338+02:00
monPolDn : uni/tn-RD/monepg-RD_Monitoring
pcTag : 49154
prio : unspecified
rn : epg-EPG_RD11
scope : 2818051
status :
triggerSt : triggerable
uid : 15374
od
admin@bdsol-aci2-apic1:fv-[uni--tn-RD--ap-App_RD1--epg-EPG_RD11]> moquery -d uni/epp/fv-[uni/tn-RD/ap-App_RD1/epg-EPG_RD11]
Total Objects shown: 1
# fv.EpP
epgPKey : uni/tn-RD/ap-App_RD1/epg-EPG_RD11
bdDefDn : uni/bd-[uni/tn-RD/BD-RD_BD1]-isSvc-no
bdDefStQual : none
childAction :
ctxDefDn :
ctxDefStQual : none
ctxSeg : 0
deplSt : deployable
descr :
dn : uni/epp/fv-[uni/tn-RD/ap-App_RD1/epg-EPG_RD11]
enfPref : hw
epgDn :
epgName : EPG_RD11
l2FDSeg : 0
l3CtxEncap : unknown
lcOwn : local
modTs : 2014-11-13T16:44:50.458+02:00
monPolDn : uni/tn-RD/monepg-RD_Monitoring
name :
npName : App_RD1
operSt : allocated
ownerKey :
ownerTag :
pcTag : 49154
prio : unspecified
rn : fv-[uni/tn-RD/ap-App_RD1/epg-EPG_RD11]
scopeId : 2818051
status :
tName : RD
Link the Resolved EPG to the
Resolved BD

## Slide 47: EPG resolved model child - fvLocale Which leaf will get the EPG ?
admin@bdsol-aci2-apic1:~> moquery -c fvLocale | grep dn | grep epg-EPG_RD11
dn : uni/epp/fv-[uni/tn-RD/ap-App_RD1/epg-EPG_RD11]/node-103
dn : uni/epp/fv-[uni/tn-RD/ap-App_RD1/epg-EPG_RD11]/node-101
dn : uni/epp/fv-[uni/tn-RD/ap-App_RD1/epg-EPG_RD11]/node-102
dn : uni/epp/fv-[uni/tn-RD/ap-App_RD1/epg-EPG_RD11]/node-104
admin@bdsol-aci2-apic1:~> moquery -d uni/epp/fv-[uni/tn-RD/ap-App_RD1/epg-EPG_RD11]/node-104
Total Objects shown: 1
# fv.Locale
id : 104
childAction :
deployAllPorts : no
dn : uni/epp/fv-[uni/tn-RD/ap-App_RD1/epg-EPG_RD11]/node-104
instrImedcy : lazy
lcOwn : local
modTs : 2014-11-13T16:44:50.458+02:00
monPolDn : uni/tn-RD/monepg-RD_Monitoring
operSt : allocated
rn : node-104
rtrId : 0.0.0.0
status :

## Slide 48: EPG resolved model – fvStPathAtt Static Path Attach
admin@bdsol-aci2-apic1:~> moquery -c fvStPathAtt | grep EPG_RD11
dn : uni/epp/fv-[uni/tn-RD/ap-App_RD1/epg-EPG_RD11]/node-101/stpathatt-[eth1/33]
dn : uni/epp/fv-[uni/tn-RD/ap-App_RD1/epg-EPG_RD11]/node-102/stpathatt-[eth1/33]
admin@bdsol-aci2-apic1:~> moquery -d uni/epp/fv-[uni/tn-RD/ap-App_RD1/epg-EPG_RD11]/node-101/stpathatt-[eth1/33]
Total Objects shown: 1
# fv.StPathAtt
pathName : eth1/33
childAction :
descr :
dn : uni/epp/fv-[uni/tn-RD/ap-App_RD1/epg-EPG_RD11]/node-101/stpathatt-[eth1/33]
lcOwn : local
modTs : 2014-11-13T16:44:50.458+02:00
monPolDn : uni/tn-RD/monepg-RD_Monitoring
name :
ownerKey :
ownerTag :
rn : stpathatt-[eth1/33]
status :
fvStPathAtt object should be created
When a static path is added to the EPG.

## Slide 49: EPG resolved model – fvDyPathAtt Dynamic Path Attach
admin@bdsol-aci2-apic1:~> moquery -c fvDyPathAtt | grep RD11
dn : uni/epp/fv-[uni/tn-RD/ap-App_RD1/epg-EPG_RD11]/node-103/dyatt-[topology/pod-1/paths-103/pathep-[eth1/47]]
dn : uni/epp/fv-[uni/tn-RD/ap-App_RD1/epg-EPG_RD11]/node-104/dyatt-[topology/pod-1/paths-104/pathep-[eth1/47]]
admin@bdsol-aci2-apic1:~> moquery -d uni/epp/fv-[uni/tn-RD/ap-App_RD1/epg-EPG_RD11]/node-103/dyatt-[topology/pod-1/paths-103/pathep-[eth1/47]]
Total Objects shown: 1
# fv.DyPathAtt
targetDn : topology/pod-1/paths-103/pathep-[eth1/47]
childAction :
descr :
dn : uni/epp/fv-[uni/tn-RD/ap-App_RD1/epg-EPG_RD11]/node-103/dyatt-[topology/pod-1/paths-103/pathep-[eth1/47]]
lcOwn : local
modTs : 2014-11-13T16:44:50.458+02:00
monPolDn : uni/tn-RD/monepg-RD_Monitoring
name :
ownerKey :
ownerTag :
pathName :
rn : dyatt-[topology/pod-1/paths-103/pathep-[eth1/47]]
status :
fvDyPathAtt object should be created
When a VMM is added to the EPG.

## Slide 50: EPG resolved model – fvIfConn Interface Connections
admin@bdsol-aci2-apic1:~> moquery -c fvIfConn | grep dn | grep RD11
dn : uni/epp/fv-[uni/tn-RD/ap-App_RD1/epg-EPG_RD11]/node-103/dyatt-[topology/pod-1/paths-103/pathep-[eth1/47]]/conndef/conn-[vxlan-8847360]-[0.0.0.0]
dn : uni/epp/fv-[uni/tn-RD/ap-App_RD1/epg-EPG_RD11]/node-101/stpathatt-[eth1/33]/conndef/conn-[vlan-2101]-[0.0.0.0]
dn : uni/epp/fv-[uni/tn-RD/ap-App_RD1/epg-EPG_RD11]/node-102/stpathatt-[eth1/33]/conndef/conn-[vlan-2101]-[0.0.0.0]
dn : uni/epp/fv-[uni/tn-RD/ap-App_RD1/epg-EPG_RD11]/node-104/dyatt-[topology/pod-1/paths-104/pathep-[eth1/47]]/conndef/conn-[vxlan-8847360]-[0.0.0.0]
dn : uni/epp/fv-[uni/tn-RD/ap-App_RD1/epg-EPG_RD11]/node-103/dyatt-[topology/pod-1/paths-103/pathep-[eth1/47]]/conndef/conn-[vxlan-8683521]-[0.0.0.0]
admin@bdsol-aci2-apic1:~>
Contains the encaps information for St and dy path

## Slide 51: EPG resolved model – fvIfConn Interface Connections Vlan
admin@bdsol-aci2-apic1:~> moquery -d uni/epp/fv-[uni/tn-RD/ap-App_RD1/epg-EPG_RD11]/node-101/stpathatt-[eth1/33]/conndef/conn-[vlan-2101]-[0.0.0.0]
Total Objects shown: 1
# fv.IfConn
encap : vlan-2101
addr : 0.0.0.0
auto : no
bcastP : 0.0.0.0
childAction :
descr :
dn : uni/epp/fv-[uni/tn-RD/ap-App_RD1/epg-EPG_RD11]/node-101/stpathatt-[eth1/33]/conndef/conn-[vlan-2101]-[0.0.0.0]
extEncap : unknown
gw : 0.0.0.0
ifInstT : l3-port
lcOwn : local
mac : 00:00:00:00:00:00
mcastAddr : 0.0.0.0
modTs : 2014-11-13T16:44:50.458+02:00
mode : regular
monPolDn : uni/tn-RD/monepg-RD_Monitoring
mtu : inherit
name :
resImedcy : lazy
rn : conn-[vlan-2101]-[0.0.0.0]
status :
validState : not-validated

## Slide 52: EPG resolved model – fvIfConn Interface Connections Vxlan
admin@bdsol-aci2-apic1:~> moquery -d uni/epp/fv-[uni/tn-RD/ap-App_RD1/epg-EPG_RD11]/node-104/dyatt-[topology/pod-1/paths-104/pathep-[eth1/47]]/conndef/conn-[vxlan-8847360]-[0.0.0.0]
Total Objects shown: 1
# fv.IfConn
encap : vxlan-8847360
addr : 0.0.0.0
auto : no
bcastP : 0.0.0.0
childAction :
descr :
dn : uni/epp/fv-[uni/tn-RD/ap-App_RD1/epg-EPG_RD11]/node-104/dyatt-[topology/pod-1/paths-104/pathep-[eth1/47]]/conndef/conn-[vxlan-8847360]-[0.0.0.0]
extEncap : unknown
gw : 0.0.0.0
ifInstT : l3-port
lcOwn : local
mac : 00:00:00:00:00:00
mcastAddr : 229.10.1.86
modTs : 2014-11-13T16:44:50.458+02:00
mode : regular
monPolDn : uni/tn-RD/monepg-RD_Monitoring
mtu : inherit
name :
resImedcy : lazy
rn : conn-[vxlan-8847360]-[0.0.0.0]
status :
validState : not-validated
For fvDyPathAtt, encaps in fvIfConn
Can be vlan or vxlan associated by VMM
Provider to the EPG (port-group)
Visible (in VMM domain inventory)

## Slide 53: Epg
fvTenant
fvBD
fvCtx
fvAp
fvAEPg
fvRsBd
fvRsCtx
fvEpP
fvBDDef
fvCtxDef
bdDn
ctxDefDn
ctxDn
bdDefDn
epgPKey
fvlocale
fvDyPathAtt
fvStPathAtt
fvIfConn
fvIfConn
fabricPathEp
l3Ctx
l2BD
vlanCktEp
vlanRsVlanEppAtt
vlanRsPathDomAtt
l2RtDomIfConn
nwPathEp
bdDefDn
epgDn
vxlanCktEp
vxlanRsVxlanEppAtt
vxlanRsPathDomAtt
l2RtDomIfConn
nwPathEp
epgDn
tdn to EpP
(res EPG)

## Slide 54: EPG concrete model – VlanCktEp Vlan in concrete model on a leaf
admin@bdsol-aci2-apic1:~> moquery -d topology/pod-1/node-102/sys/ctx-[vxlan-2818051]/bd-[vxlan-16514958]/vlan-[vlan-2101]
# vlan.CktEp
encap : vlan-2101
adminSt : active
childAction :
createTs : 2014-11-13T13:21:46.000+02:00
ctrl : policy-enforced
dn : topology/pod-1/node-102/sys/ctx-[vxlan-2818051]/bd-[vxlan-16514958]/vlan-[vlan-2101]
enfPref : hw
epgDn : uni/tn-RD/ap-App_RD1/epg-EPG_RD11
fabEncap : vxlan-8592
hwId : 19
id : 17
lcOwn : local
modTs : 2014-11-13T16:44:50.532+02:00
mode : CE
monPolDn : uni/tn-RD/monepg-RD_Monitoring
name : RD:App_RD1:EPG_RD11
operSt : up
operStQual : unspecified
operState : disabled
pcTag : 49154
qosPrio : unspecified
qosmCfgFailedBmp :
qosmCfgFailedTs : 00:00:00:00.000
qosmCfgState : 0
rn : vlan-[vlan-2101]
status :
type : ckt-vlan
vlanmgrCfgFailedBmp :
vlanmgrCfgFailedTs : 00:00:00:00.000
vlanmgrCfgState : 0

## Slide 55: EPG concrete model – vlanRsVlanEppAtt linking concrete vlan to resolved EPG
admin@bdsol-aci2-apic1:vlan-[vlan-2101]> moquery -c vlanRsVlanEppAtt | grep dn | grep vlan-2101
dn : topology/pod-1/node-102/sys/ctx-[vxlan-2818051]/bd-[vxlan-16514958]/vlan-[vlan-2101]/rsvlanEppAtt
dn : topology/pod-1/node-101/sys/ctx-[vxlan-2818051]/bd-[vxlan-16514958]/vlan-[vlan-2101]/rsvlanEppAtt
admin@bdsol-aci2-apic1:vlan-[vlan-2101]> moquery -d topology/pod-1/node-102/sys/ctx-[vxlan-2818051]/bd-[vxlan-16514958]/vlan-[vlan-2101]/rsvlanEppAtt
Total Objects shown: 1
# vlan.RsVlanEppAtt
childAction :
dn : topology/pod-1/node-102/sys/ctx-[vxlan-2818051]/bd-[vxlan-16514958]/vlan-[vlan-2101]/rsvlanEppAtt
forceResolve : no
lcOwn : local
modTs : 2014-11-13T13:21:49.649+02:00
parentSKey : 17
rType : mo
rn : rsvlanEppAtt
state : formed
stateQual : none
status :
tCl : fvEpP
tDn : uni/epp/fv-[uni/tn-RD/ap-App_RD1/epg-EPG_RD11]
tType : mo

## Slide 56: EPG concrete model – l2RsPathDomAt linking concrete vlan to physical port
admin@bdsol-aci2-apic1> moquery -c l2RsPathDomAtt | grep dn | grep vlan-2101
dn : topology/pod-1/node-102/sys/ctx-[vxlan-2818051]/bd-[vxlan-16514958]/vlan-[vlan-2101]/rspathDomAtt-[topology/pod-1/node-102/sys/conng/path-[eth1/33]]
dn : topology/pod-1/node-101/sys/ctx-[vxlan-2818051]/bd-[vxlan-16514958]/vlan-[vlan-2101]/rspathDomAtt-[topology/pod-1/node-101/sys/conng/path-[eth1/33]]
admin@bdsol-aci2-apic1>
admin@bdsol-aci2-apic1:vlan-[vlan-2101]> moquery -d topology/pod-1/node-102/sys/ctx-[vxlan-2818051]/bd-[vxlan-16514958]/vlan-[vlan-2101]/rspathDomAtt-[topology/pod-1/node-102/sys/conng/path-[eth1/33]]
Total Objects shown: 1
# l2.RsPathDomAtt
tDn : topology/pod-1/node-102/sys/conng/path-[eth1/33]
childAction :
dn : topology/pod-1/node-102/sys/ctx-[vxlan-2818051]/bd-[vxlan-16514958]/vlan-[vlan-2101]/rspathDomAtt-[topology/pod-1/node-102/sys/conng/path-[eth1/33]]
forceResolve : no
lcOwn : local
modTs : 2014-11-13T16:44:50.532+02:00
monPolDn : uni/tn-RD/monepg-RD_Monitoring
parentSKey : 17
rType : mo
rn : rspathDomAtt-[topology/pod-1/node-102/sys/conng/path-[eth1/33]]
state : formed
stateQual : none
status :
tCl : nwPathEp
tSKey : eth1/33
tType : mo
type : regular
vlanmgrCfgFailedBmp :
vlanmgrCfgFailedTs : 00:00:00:00.000
vlanmgrCfgState : 0

## Slide 57: EPG concrete model – l2RtDomIfConn linking concrete vlan to resolved static path
admin@bdsol-aci2-apic1:vlan-[vlan-2101]> moquery -c l2RtDomIfConn | grep dn | grep 2101
dn : topology/pod-1/node-102/sys/ctx-[vxlan-2818051]/bd-[vxlan-16514958]/vlan-[vlan-2101]/rtfvDomIfConn-[uni/epp/fv-[uni/tn-RD/ap-App_RD1/epg-EPG_RD11]/node-102/stpathatt-[eth1/33]/conndef/conn-[vlan-2101]-[0.0.0.0]]
dn : topology/pod-1/node-101/sys/ctx-[vxlan-2818051]/bd-[vxlan-16514958]/vlan-[vlan-2101]/rtfvDomIfConn-[uni/epp/fv-[uni/tn-RD/ap-App_RD1/epg-EPG_RD11]/node-101/stpathatt-[eth1/33]/conndef/conn-[vlan-2101]-[0.0.0.0]]
admin@bdsol-aci2-apic1:vlan-[vlan-2101]> moquery -d topology/pod-1/node-102/sys/ctx-[vxlan-2818051]/bd-[vxlan-16514958]/vlan-[vlan-2101]/rtfvDomIfConn-[uni/epp/fv-[uni/tn-RD/ap-App_RD1/epg-EPG_RD11]/node-102/stpathatt-[eth1/33]/conndef/conn-[vlan-2101]-[0.0.0.0]]
Total Objects shown: 1
# l2.RtDomIfConn
tDn : uni/epp/fv-[uni/tn-RD/ap-App_RD1/epg-EPG_RD11]/node-102/stpathatt-[eth1/33]/conndef/conn-[vlan-2101]-[0.0.0.0]
childAction :
dn : topology/pod-1/node-102/sys/ctx-[vxlan-2818051]/bd-[vxlan-16514958]/vlan-[vlan-2101]/rtfvDomIfConn-[uni/epp/fv-[uni/tn-RD/ap-App_RD1/epg-EPG_RD11]/node-102/stpathatt-[eth1/33]/conndef/conn-[vlan-2101]-[0.0.0.0]]
lcOwn : local
modTs : 2014-11-13T13:21:49.649+02:00
parentSKey : 17
rn : rtfvDomIfConn-[uni/epp/fv-[uni/tn-RD/ap-App_RD1/epg-EPG_RD11]/node-102/stpathatt-[eth1/33]/conndef/conn-[vlan-2101]-[0.0.0.0]]
status :
tCl : fvIfConn

## Slide 58: Epg
fvTenant
fvBD
fvCtx
fvAp
fvAEPg
fvRsBd
fvRsCtx
fvEpP
fvBDDef
fvCtxDef
bdDn
ctxDefDn
ctxDn
bdDefDn
epgPKey
fvlocale
fvDyPathAtt
fvStPathAtt
fvIfConn
fvIfConn
fabricPathEp
l3Ctx
l2BD
vlanCktEp
vlanRsVlanEppAtt
vlanRsPathDomAtt
l2RtDomIfConn
nwPathEp
bdDefDn
epgDn
vxlanCktEp
vxlanRsVxlanEppAtt
vxlanRsPathDomAtt
l2RtDomIfConn
nwPathEp
epgDn
tdn to EpP
(res EPG)

## Slide 59: EPG concrete model – vxlanCktEp
admin@bdsol-aci2-apic1:~> moquery -c vxlanCktEp | grep dn | grep 8847360
dn : topology/pod-1/node-103/sys/ctx-[vxlan-2818051]/bd-[vxlan-16514958]/vxlan-[vxlan-8847360]
dn : topology/pod-1/node-104/sys/ctx-[vxlan-2818051]/bd-[vxlan-16514958]/vxlan-[vxlan-8847360]
admin@bdsol-aci2-apic1:~> topology/pod-1/node-103/sys/ctx-[vxlan-2818051]/bd-[vxlan-16514958]/vxlan-[vxlan-8847360]
# vxlan.CktEp
encap : vxlan-8847360
adminSt : active
childAction :
createTs : 2014-11-12T17:42:13.000+02:00
ctrl : policy-enforced
dn : topology/pod-1/node-103/sys/ctx-[vxlan-2818051]/bd-[vxlan-16514958]/vxlan-[vxlan-8847360]
enfPref : hw
epgDn : uni/tn-RD/ap-App_RD1/epg-EPG_RD11
hwId : 14
id : 12
lcOwn : local
mcastEncap : 229.10.1.86
modTs : 2014-11-13T16:44:50.534+02:00
mode : CE
monPolDn : uni/tn-RD/monepg-RD_Monitoring
name : RD:App_RD1:EPG_RD11
operSt : up
pcTag : 49154
qosPrio : unspecified
rn : vxlan-[vxlan-8847360]
status :
type : ckt-vxlan
vlanmgrCfgFailedBmp :
vlanmgrCfgFailedTs : 00:00:00:00.000
vlanmgrCfgState : 0

## Slide 60: EPG concrete model – vxlanRsVxlanEppAtt linking concrete vxlan to resolved EPG
admin@bdsol-aci2-apic1:vxlan-[vxlan-8847360]> moquery -c vxlanRsVxlanEppAtt | grep dn | grep vxlan-884
dn : topology/pod-1/node-103/sys/ctx-[vxlan-2818051]/bd-[vxlan-16514958]/vxlan-[vxlan-8847360]/rsvxlanEppAtt
dn : topology/pod-1/node-104/sys/ctx-[vxlan-2818051]/bd-[vxlan-16514958]/vxlan-[vxlan-8847360]/rsvxlanEppAtt
admin@bdsol-aci2-apic1:vxlan-[vxlan-8847360]>
admin@bdsol-aci2-apic1:vxlan-[vxlan-8847360]> moquery -d topology/pod-1/node-103/sys/ctx-[vxlan-2818051]/bd-[vxlan-16514958]/vxlan-[vxlan-8847360]/rsvxlanEppAtt
Total Objects shown: 1
# vxlan.RsVxlanEppAtt
childAction :
dn : topology/pod-1/node-103/sys/ctx-[vxlan-2818051]/bd-[vxlan-16514958]/vxlan-[vxlan-8847360]/rsvxlanEppAtt
forceResolve : no
lcOwn : local
modTs : 2014-11-12T17:42:17.695+02:00
parentSKey : 12
rType : mo
rn : rsvxlanEppAtt
state : formed
stateQual : none
status :
tCl : fvEpP
tDn : uni/epp/fv-[uni/tn-RD/ap-App_RD1/epg-EPG_RD11]
tType : mo

## Slide 61: EPG concrete model – l2RsPathDomAtt linking encaps vxlan to Physical port
admin@bdsol-aci2-apic1:vxlan-[vxlan-8847360]> moquery -c l2RsPathDomAtt | grep dn | grep 884
dn : topology/pod-1/node-103/sys/ctx-[vxlan-2818051]/bd-[vxlan-16514958]/vxlan-[vxlan-8847360]/rspathDomAtt-[topology/pod-1/node-103/sys/conng/path-[eth1/47]]
dn : topology/pod-1/node-104/sys/ctx-[vxlan-2818051]/bd-[vxlan-16514958]/vxlan-[vxlan-8847360]/rspathDomAtt-[topology/pod-1/node-104/sys/conng/path-[eth1/47]]
admin@bdsol-aci2-apic1:vxlan-[vxlan-8847360]> moquery -d topology/pod-1/node-103/sys/ctx-[vxlan-2818051]/bd-[vxlan-16514958]/vxlan-[vxlan-8847360]/rspathDomAtt-[topology/pod-1/node-103/sys/conng/path-[eth1/47]]
# l2.RsPathDomAtt
tDn : topology/pod-1/node-103/sys/conng/path-[eth1/47]
childAction :
dn : topology/pod-1/node-103/sys/ctx-[vxlan-2818051]/bd-[vxlan-16514958]/vxlan-[vxlan-8847360]/rspathDomAtt-[topology/pod-1/node-103/sys/conng/path-[eth1/47]]
forceResolve : no
lcOwn : local
modTs : 2014-11-13T16:44:50.534+02:00
monPolDn : uni/tn-RD/monepg-RD_Monitoring
parentSKey : 12
rType : mo
rn : rspathDomAtt-[topology/pod-1/node-103/sys/conng/path-[eth1/47]]
state : formed
stateQual : none
status :
tCl : nwPathEp
tSKey : eth1/47
tType : mo
type : regular
vlanmgrCfgFailedBmp :
vlanmgrCfgFailedTs : 00:00:00:00.000
vlanmgrCfgState : 0

## Slide 62: EPG concrete model – l2RtDomIfConn linking concrete vxlan to resolved dyn path
admin@bdsol-aci2-apic1:~> moquery -c l2RtDomIfConn | grep dn | grep vxlan-8847360
dn : topology/pod-1/node-104/sys/ctx-[vxlan-2818051]/bd-[vxlan-16514958]/vxlan-[vxlan-8847360]/rtfvDomIfConn-[uni/epp/fv-[uni/tn-RD/ap-App_RD1/epg-EPG_RD11]/node-104/dyatt-[topology/pod-1/paths-104/pathep-[eth1/47]]/conndef/conn-[vxlan-8847360]-[0.0.0.0]]
dn : topology/pod-1/node-103/sys/ctx-[vxlan-2818051]/bd-[vxlan-16514958]/vxlan-[vxlan-8847360]/rtfvDomIfConn-[uni/epp/fv-[uni/tn-RD/ap-App_RD1/epg-EPG_RD11]/node-103/dyatt-[topology/pod-1/paths-103/pathep-[eth1/47]]/conndef/conn-[vxlan-8847360]-[0.0.0.0]]
admin@bdsol-aci2-apic1:~> moquery -d topology/pod-1/node-103/sys/ctx-[vxlan-2818051]/bd-[vxlan-16514958]/vxlan-[vxlan-8847360]/rtfvDomIfConn-[uni/epp/fv-[uni/tn-RD/ap-App_RD1/epg-EPG_RD11]/node-103/dyatt-[topology/pod-1/paths-103/pathep-[eth1/47]]/conndef/conn-[vxlan-8847360]-[0.0.0.0]]
Total Objects shown: 1
# l2.RtDomIfConn
tDn : uni/epp/fv-[uni/tn-RD/ap-App_RD1/epg-EPG_RD11]/node-103/dyatt-[topology/pod-1/paths-103/pathep-[eth1/47]]/conndef/conn-[vxlan-8847360]-[0.0.0.0]
childAction :
dn : topology/pod-1/node-103/sys/ctx-[vxlan-2818051]/bd-[vxlan-16514958]/vxlan-[vxlan-8847360]/rtfvDomIfConn-[uni/epp/fv-[uni/tn-RD/ap-App_RD1/epg-EPG_RD11]/node-103/dyatt-[topology/pod-1/paths-103/pathep-[eth1/47]]/conndef/conn-[vxlan-8847360]-[0.0.0.0]]
lcOwn : local
modTs : 2014-11-12T17:42:17.695+02:00
parentSKey : 12
rn : rtfvDomIfConn-[uni/epp/fv-[uni/tn-RD/ap-App_RD1/epg-EPG_RD11]/node-103/dyatt-[topology/pod-1/paths-103/pathep-[eth1/47]]/conndef/conn-[vxlan-8847360]-[0.0.0.0]]
status :
tCl : fvIfConn

## Slide 63: Example – ref
Some bugs where resolved/concrete model do not follow logical
CSCur31409(CSC.datacenter,R-V,rducombl)stuck MO class : fvDyPathAtt when the access policy is deleted
CSCur60990(CSC.datacenter,upd,cdetsbsi)stuck MO fabric.Link after decommission
CSCur35477(CSC.datacenter,new,cdetsbsi)AVS - fvDyPathAtt and FD_VXLAN not created for one EPG
CSCur31133(CSC.datacenter,new,cdetsbsi)stuck concrete MO after deletion of MO of class infraAccBndlGrp
https://techzone.cisco.com/t5/Application-Centric/Class-amp-Object-Configuration-Verification-Case-Example/ta-p/729533